## Slide 1: Digital Integrated Circuits Designing Combinational Logic Circuits Fuyuzhuo

## Slide 2: Combinational vs. Sequential Logic
Combinational
Sequential
Output =
f
(
In
)
Output =
f
(
In, Previous In
)

## Slide 3: agenda
Static CMOS design
Ratioed logic design-Pseudo NMOS
Pass transistor design
Dynamic logic

## Slide 4: agenda
Static CMOS design
Ratioed logic design___Pseudo NMOS
Pass transistor design
Dynamic logic
What is the difference between inverter and logic?

## Slide 5: Static CMOS logic
CMOS static characteristic
CMOS propagate delay
Large fan-in technology
Logic effort
CMOS power analysis

## Slide 6: Static CMOS Circuit
Gate output is connected to either VDD or VSS via a low-resistive path*
Contrast to the dynamic circuit class, which relies on temporary storage of signal values on the capacitance of high impedance circuit nodes
* except during the switching transients

## Slide 7: Standard Cell Layout Methodology
signals
Routing
channel
VDD
GND
What logic function is this?
Notes: Route VDD and GND horizontally
Route singals in poly perpendicular to VDD and GND (vertically) – poly can serve as input to both nfets and pfets
Order inputs (consistent Euler path) to optimize the horizontal connectivity of diff strips
want unbroken row of devices with abutting source/drain connections – so there is only one strip of diffusion in both wells
3) Place diffs in horizontal strips
4) Interconnect appropriately
Interconnect between cells are done in “routing channels”
Contacts and wells not shown.
What does this implement?? (NAND feeding an Inverter – so an AND)

## Slide 8: OAI21 Logic Graph
C
A
B
X = !(C • (A + B))
B
A
C
i
j
j
VDD
X
X
i
GND
A
B
C
PUN
PDN
A
B
C
Notes: Systematic approach to derive order of input signal wires so gate can be laid out to minimize area
Note PUN and PDN are duals (parallel <-> series)
Vertices are nodes (signals) of circuit, VDD, X, GND and edges are transitions

## Slide 9: Two Stick Layouts of !(C • (A + B))
A
B
C
X
VDD
GND
X
C
A
B
VDD
GND
uninterrupted diffusion strip
interrupt
Notes: Line of diffusion layout – abutting source-drain connections
Note crossover of left layout eliminated by A B C ordering – talk about area needed for via (and speed impact due to via resistance)

## Slide 10: Consistent Euler Path
j
VDD
X
X
i
GND
A
B
C
For a single poly strip for every input signal, the Euler paths in the PUN and PDN must be consistent (the same)
An uninterrupted diffusion strip is possible only if there exists a Euler path in the logic graph
  Euler path: a path through all nodes in the graph such that each edge is visited once and only once

## Slide 11: Consistent Euler Path
j
VDD
X
X
i
GND
A
B
C
A
B
C
For a single poly strip for every input signal, the Euler paths in the PUN and PDN must be consistent (the same)
An uninterrupted diffusion strip is possible only if there exists a Euler path in the logic graph
  Euler path: a path through all nodes in the graph such that each edge is visited once and only once
Notes: A path through all nodes in the graph such that each edge is visited once and only once.
The sequence of signals on the path is the signal ordering for the inputs.
PUN and PDN Euler paths are (must be) consistent (same sequence)
If you can define a Euler path then you can generate a layout with no diffusion breaks
A B C
C A B
B C A  no PDN -> show how with ppt pen drawing
B A C
A C B -> no PDN
C B A

## Slide 12: OAI22 Logic Graph
C
A
B
X = !((A+B)•(C+D))
B
A
D
VDD
X
X
GND
A
B
C
PUN
PDN
C
D
D
A
B
C
D
Notes: Consistent Euler paths
ABDC
BDCA
DCAB
CABD
BACD
ACDB
CDBA
DBAC
and NOT DACB, BCAD, etc.

## Slide 13: OAI22 Layout
B
A
D
VDD
GND
C
X
Some functions have no consistent Euler path like
x = !(a + bc + de) (but x = !(bc + a + de) does!)
Notes: Can you draw the Euler diagrams for both and show the consistent Euler path(s) for the second?

## Slide 14: VTC is Data-Dependent
The threshold voltage of M2 is higher than M1 due to the body effect ()
VTn2 = VTn0 + ((|2F| + Vint) - |2F|)
since VSB of M2 is not zero (when VB = 0) due to the presence of Cint
VTn1 = VTn0
Notes: VTC characteristics are dependent upon the data input patterns applied to the gate (so the noise margins are also data dependent!)
Threshold voltage of M2 will be higher than transistor M1 due to body effect
Case 1 – both transistors in the PUN are on simultaneously for A=B=0, representing a strong pull-up. In the other two cases only one of the pull-up devices is on. So the VTC is shifted left as a result of the weaker PUN for the second and third cases.
Case 2 – see Case 3, small difference can be attributed to the body effect of M2 and the drive voltage
Case 3 – M2 as resistor in series with M1, so only small effect on VTC; since pulldown is strong and pullup weaker than case 1, VTC shifted to the left
(also have to discharge both CL (on the output) and Cint (possibly) thru M1 so will also be slower!)

## Slide 15: VTC is Data-Dependent
Notes: VTC characteristics are dependent upon the data input patterns applied to the gate (so the noise margins are also data dependent!)
Threshold voltage of M2 will be higher than transistor M1 due to body effect
Case 1 – both transistors in the PUN are on simultaneously for A=B=0, representing a strong pull-up. In the other two cases only one of the pull-up devices is on. So the VTC is shifted left as a result of the weaker PUN for the second and third cases.
Case 2 – see Case 3, small difference can be attributed to the body effect of M2 and the drive voltage
Case 3 – M2 as resistor in series with M1, so only small effect on VTC; since pulldown is strong and pullup weaker than case 1, VTC shifted to the left
(also have to discharge both CL (on the output) and Cint (possibly) thru M1 so will also be slower!)

## Slide 16: VTC is Data-Dependent
Notes: VTC characteristics are dependent upon the data input patterns applied to the gate (so the noise margins are also data dependent!)
Threshold voltage of M2 will be higher than transistor M1 due to body effect
Case 1 – both transistors in the PUN are on simultaneously for A=B=0, representing a strong pull-up. In the other two cases only one of the pull-up devices is on. So the VTC is shifted left as a result of the weaker PUN for the second and third cases.
Case 2 – see Case 3, small difference can be attributed to the body effect of M2 and the drive voltage
Case 3 – M2 as resistor in series with M1, so only small effect on VTC; since pulldown is strong and pullup weaker than case 1, VTC shifted to the left
(also have to discharge both CL (on the output) and Cint (possibly) thru M1 so will also be slower!)

## Slide 17: CMOS Properties
Full rail-to-rail swing high noise margins
not dependent upon device sizes ratioless
Always a path to Vdd or Gnd low output impedance
zero steady-state input current high input resistance
No direct path steady state no static power
Propagation delay function of load capacitance and resistance of transistors

## Slide 18: Static CMOS logic
CMOS static characteristic
CMOS propagate delay
Large fan-in technology
Logic effort
CMOS power analysis

## Slide 19: Delay Definitions
tpdr: rising propagation delay
  From input to rising output crossing VDD/2
tpdf: falling propagation delay
  From input to falling output crossing VDD/2
tpd: average propagation delay(max-time)
  tpd = (tpdr + tpdf)/2
tr: rise time
  From output crossing 0.1 VDD to 0.9 VDD
tf: fall time
  From output crossing 0.9 VDD to 0.1 VDD

## Slide 20: Delay Definitions
tcdr: rising contamination delay
  Minimum time from input to rising output crossing VDD/2
tcdf: falling contamination delay
  Minimum time from input to falling output crossing VDD/2
tcd: average contamination delay(min-time)
  Minimum time from input crossing 50% to the output crossing 50%
  tpd = (tcdr + tcdf)/2

## Slide 21: Simulated Inverter Delay
Solving differential equations by hand is too hard
SPICE simulator solves the equations numerically
  Uses more accurate I-V models too!
But simulations take time to write

## Slide 22: Why we need estimation?
We have timing analyzer at different levels
  The architectural/micro-architectual level
  Logic level
  Circuit level
  Layout level
GIGO(Garbage In Garbage Out)!
Simulation could only tell how fast…, it could not tell how to modify the circuit

## Slide 23: Delay Estimation
We would like to be able to easily estimate delay
  Not as accurate as simulation
  But easier to ask “What if?”
The step response usually looks like a 1st order RC response with a decaying exponential.
Use RC delay models to estimate delay
  C = total capacitance on output node
  Use effective resistance R
  So that tpd = RC
Characterize transistors by finding their effective R
  Depends on average current as gate switches

## Slide 24: Input Pattern Effects on Delay
Delay is dependent on the pattern of inputs
Low to high transition
  both inputs go low
    delay is 0.69 Rp/2 CL
  one input goes low
    delay is 0.69 Rp CL
High to low transition
  both inputs go high
    delay is 0.69 2Rn CL
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint

## Slide 25: Transistor Sizing
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint
B
Rp
A
Rp
A
Rn
B
Rn
CL
Cint
2
2
2
2
1
1
4
4
Minimum timing
Balance between Pullup and Pulldown Network
Notes: Assumes Rp = Rn

## Slide 26: Sizing has different options
OUT = D + A • (B + C)
D
A
B
C
D
A
B
C
1
2
2
2
4
4
8
8
6
3
6
6
Notes: For class lecture.
Red sizing assuming Rp = Rn
Follow short path first; note PMOS for C and B 4 rather than 3 – average in pull-up chain of three – (4+4+2)/3 = 3
Also note structure of pull-up and pull-down to minimize diffusion cap at output (e.g., single PMOS drain connected to output)
Green for symmetric response and for performance (where Rn = 3 Rp)
Sizing rules of thumb
PMOS = 3 * NMOS
1 in series = 1
2 in series = 2
3 in series = 3
etc.

## Slide 27: Elmore Delay
ON transistors look like resistors
Pullup or pulldown network modeled as RC ladder
Elmore delay of RC ladder

## Slide 28: RC Delay Models
Use equivalent circuits for MOS transistors
  Ideal switch + capacitance and ON resistance
  Unit nMOS has resistance R, capacitance C
  Unit pMOS has resistance 2R, capacitance C
Capacitance proportional to width
Resistance inversely proportional to width

## Slide 29: Example: 3-input NAND
Sketch a 3-input NAND with transistor widths chosen to achieve effective rise and fall resistances equal to a unit inverter (R)

## Slide 30: Example: 3-input NAND
Sketch a 3-input NAND with transistor widths chosen to achieve effective rise and fall resistances equal to a unit inverter (R)

## Slide 31: Example: 3-input NAND
Sketch a 3-input NAND with transistor widths chosen to achieve effective rise and fall resistances equal to a unit inverter (R)

## Slide 32: 3-input NAND Caps
Annotate the 3-input NAND gate with gate and diffusion capacitance.

## Slide 33: 3-input NAND Caps
Annotate the 3-input NAND gate with gate and diffusion capacitance.

## Slide 34: Example: 2-input NAND
Estimate worst-case rising and falling delay of 2-input NAND driving h identical gates.

## Slide 35: Example: 2-input NAND
Estimate rising and falling propagation delays of a 2-input NAND driving h identical gates.

## Slide 36: Example: 2-input NAND
Estimate rising and falling propagation delays of a 2-input NAND driving h identical gates.
✓
✓

## Slide 37: Contamination Delay
Best-case (contamination) delay can be substantially less than propagation delay.
Ex: If both inputs fall simultaneously
✓
✓
✓
✓

## Slide 38: Practice:
1. Sketch a 4-input NAND gate with transistor widths chosen to achieve effective rise and fall resistance equal to a unit inverter.
  Compute the tLH and tHL propagation delays(in terms of R and C) of the NAND gate driving h identical NAND gates using the ELMORE delay model
A:
tpHL=ln2[4C*R/4+2R/4*4C+3R/4*4C+4R/4*(12C+6Ch)]=RCln2[1+2+3+(12+6h)]=ln2(18+6h)
tpLH=ln2[4C*R+4C*R+4C*R+ (12C+6Ch) R*]=RCln2[24+6h]

## Slide 39: Layout Comparison
Which layout is better?

## Slide 40: Diffusion Capacitance
assumed contacted diffusion on every s / d.
Good layout minimizes diffusion area
Ex: NAND3 layout shares one diffusion contact
  Reduces output capacitance by 2C
  Merged uncontacted diffusion might help too

## Slide 41: Fan-In Considerations
D
C
B
A
D
C
B
A
CL
C3
C2
C1
Distributed RC model
(Elmore delay)
tpHL = 0.69 Reqn(C1+2C2+3C3+4CL)
Propagation delay deteriorates rapidly as a function of fan-in quadratically in the worst case
Notes: While output capacitance makes full swing transition (from VDD to 0), internal nodes only transition from VDD-VTn to GND
C1, C2, C3 on the order of 0.85 fF for W/L of 0.5/0.25 NMOS and 0.375/0.25 PMOS
CL of 3.2 fF with no output load (all diffusion capacitance – intrinsic capacitance of the gate itself).
To give a 80.3 psec tpHL (simulated as 86 psec)

## Slide 42: Worst case of tpLH
D
C
B
A
A=1
CL
C3
C2
C1
B=1
C=1
D=1→0
𝛕 =2R/2*(2NC+Cext)+2R/2*NC*N=2NRC+RCext +N2RC
Notes: While output capacitance makes full swing transition (from VDD to 0), internal nodes only transition from VDD-VTn to GND
C1, C2, C3 on the order of 0.85 fF for W/L of 0.5/0.25 NMOS and 0.375/0.25 PMOS
CL of 3.2 fF with no output load (all diffusion capacitance – intrinsic capacitance of the gate itself).
To give a 80.3 psec tpHL (simulated as 86 psec)

## Slide 43: tp as a function of fan-In and fan-out
Fan-in: quadratic due to increasing resistance and capacitance
Fan-out: each additional fan-out gate adds two gate capacitances to CL
tp = a1FI + a2FI2 + a3FO
Notes: a1 term is for parallel chain, a2 term is for serial chain, a3 is fan-out

## Slide 44: Delay Dependence on Input Patterns
A=B=10
A=1, B=10
A=1 0, B=1
time [ps]
Voltage [V]
Input Data Pattern | Delay (psec)
A=B=01 | 69(max)
A=1, B=01 | 62
A= 01, B=1 | 50
A=B=10 | 35(min)
A=1, B=10 | 76
A= 10, B=1 | 57
NMOS = 0.5m/0.25 m
PMOS = 0.75m/0.25 m
CL = 100 fF
Shared cap. charging
Shared cap. discharging
Notes: A=b=0->1与a=1,b=0->1的不同在于后者只要B一变化就开始放电，而前者需要等到A导通了才能放电
Gate sizing should result in approximately equal worst case rise and fall times.
Reason for difference in the last two delays is due to internal node capacitance of the pulldown stack. When A transitions, the pullup only has to charge CL; when A=1 and B transitions pullup have to charge up both CL and Cint.
For high to low transitions (first three cases) delay depends on state of internal node. Worst case happens when internal node is charged up to VDD – VTn.
Conclusions: Estimates of delay can be fairly complex – have to consider internal node capacitances and the data patterns.

## Slide 45: Static CMOS logic
CMOS static characteristic
CMOS propagate delay
Large fan-in technology
Logic effort
CMOS power analysis

## Slide 46: How to choose design techniques for large fan-in
Larger parasitic capacitor, larger load to the preceding gate
Load is dominated by fan-out, the design technique makes sense
Solution
  Progressive transistor sizing
  Transistor ordering
  Alternative logic structures
  Isolating fan-in from fan-out using buffer insertion

## Slide 47: Transistor ordering
C2
C1
In1
In2
In3
M1
M2
M3
CL
C2
C1
In3
In2
In1
M1
M2
M3
CL
critical path
critical path
charged
1
01
charged
charged
1
delay determined by time to discharge CL, C1 and C2
delay determined by time to discharge CL
1
1
01
charged
discharged
discharged
Notes: For lecture.
Critical input is latest arriving signal
Place latest arriving signal (critical path) closest to the output

## Slide 48: Progressive sizing
Distributed RC line
  M1 > M2 > M3 > … > MN
the closest to the output is the smallest
Can reduce delay by more than 20%; decreasing gains as technology shrinks
Notes: M1 have to carry the discharge current from M2, M3, … MN and CL so make it the largest
MN only has to discharge the current from MN (no internal capacitances)

## Slide 49: Alternative logic structures
F = ABCDEFGH
Notes: Reduced fan-in -> deeper logic depth
Reduction in fan-in offsets, by far, the extra delay incurred by the NOR gate (second configuration).
Only simulation will tell which of the last two configurations is faster, lower power

## Slide 50: Isolating fan-in from fan-out using buffer insertion
CL
CL
Large fan-in
Large fan-out
isolating
Notes: Reduce CL on large fan-in gates, especially for large CL, and size the inverters progressively to handle the CL more effectively