## Slide 1: Digital Integrated Circuits Designing Combinational Logic Circuits Fuyuzhuo

## Slide 2: Static CMOS logic
CMOS static characteristic
CMOS propagate delay
Large fan-in technology
Logic effort
CMOS power analysis

## Slide 3: Sizing Logic Paths for Speed
Example:
  ALU load in an Intel’s microprocessor is 0.5pF
How to size the ALU datapath to achieve maximum speed?
We have already solved this for the inverter chain
Can we generalize it for any type of logic?

## Slide 4: Modified formula

## Slide 5: Modified formula
Electric effort
logic effort
Intrinsic ratio
Rpar=Rinv
Unit inverter delay

## Slide 6: Logic effort is related with… …
Transistor’s size?
the special Path?
the special edge?

## Slide 7: Outline about logic effort
Introduction
Delay in a Logic Gate
Multistage Logic Networks
Choosing the Best Number of Stages
Example
Summary

## Slide 8: Introduction
Chip designers face a bewildering array of choices
  What is the best circuit topology for a function?
  How many stages of logic give least delay?
  How wide should the transistors be?
Logical effort is a method to make these decisions
  Uses a simple model of delay
  Allows back-of-the-envelope calculations
  Helps make rapid comparisons between alternatives
  Emphasizes remarkable symmetries

## Slide 9: Example
Ben Bitdiddle is the memory designer for the Motoroil 68W86, an embedded automotive processor. Help Ben design the decoder for a register file.
Decoder specifications:
  16 word register file
  Each word is 32 bits wide
  Each bit presents load of 3 unit-sized transistors
  True and complementary address inputs A[3:0]
  Each input may drive 10 unit-sized transistors
Ben needs to decide:
  How many stages to use?
  How large should each gate be?
  How fast can decoder operate?

## Slide 10: Delay in a Logic Gate
Express delays in process-independent unit
t = 3RC
 12 ps in 180 nm process
40 ps in 0.6 mm process

## Slide 11: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components

## Slide 12: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components
Effort delay h= gf (a.k.a. stage effort)
  Again has two components

## Slide 13: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components
g: logical effort
  Measures relative ability of gate to deliver current
  g  1 for inverter

## Slide 14: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components

## Slide 15: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components
Effort delay h= gf (a.k.a. stage effort)
  Again has two components
  f: electrical effort (or called fanout)= Cout / Cin
  Ratio of output to input capacitance

## Slide 16: Delay in a Logic Gate
Express delays in process-independent unit
Delay has two components
Parasitic delay p
  Represents delay of gate driving no load
  Set by internal parasitic capacitance

## Slide 17: Delay Plots
d = p + h
  = p + fg

## Slide 18: Delay Plots
d = h + p
  = gf + p
What about NOR2?

## Slide 19: Computing Logical Effort
DEF: Logical effort is the ratio of the input capacitance of a gate to the input capacitance of an inverter delivering the same output current.
Measure from delay vs. fanout plots
Or estimate by counting transistor widths

## Slide 20: Catalog of Gates
Gate type | Number of inputs |  |  |  | 
 | 1 | 2 | 3 | 4 | n
Inverter | 1 |  |  |  | 
NAND |  | 4/3 | 5/3 | 6/3 | (n+2)/3
NOR |  | 5/3 | 7/3 | 9/3 | (2n+1)/3
Tristate / mux | 2 | 2 | 2 | 2 | 2

## Slide 21: Catalog of Gates
Gate type | Number of inputs |  |  |  | 
 | 1 | 2 | 3 | 4 | n
Inverter | 1 |  |  |  | 
NAND |  | 2 | 3 | 4 | n
NOR |  | 2 | 3 | 4 | n
Tristate / mux | 2 | 4 | 6 | 8 | 2n
Parasitic delay of common gates
  In multiples of pinv (1)

## Slide 22: Example: FO4 Inverter
Estimate the delay of a fanout-of-4 (FO4) inverter
Logical Effort: g = 1
Electrical Effort: f = 4
Parasitic Delay: p = 1
Stage Delay: d = 5
the FO4 delay is about
200 ps in 600nm process
60 ps in a 180nm process
f/3 ps in an f mm process

## Slide 23: Multistage Logic Networks
Logical effort generalizes to multistage networks
Path Logical Effort
Path Electrical Effort
Path Effort

## Slide 24: Multistage Logic Networks
Logical effort generalizes to multistage networks
Path Logical Effort
Path Electrical Effort
Path Effort
Can we write H = GF?
  F counts once and f not.

## Slide 25: Paths that Branch
G =
F =
GF =
f1 =
f2 =
H =

## Slide 26: Paths that Branch
G = 1
F = 90 / 5 = 18
GF = 18
f1 = (15 +15) / 5 = 6
f2 = 90 / 15 = 6
H = g1g2f1f2 = 36 = 2GF
No! Consider paths that branch

## Slide 27: Multistage Logic Networks
Can we write H = GF?
  F count once and f not.
H >=GF

## Slide 28: Branching Effort
Introduce branching effort
  Accounts for branching between stages in path
Now we compute the path effort
  H = GBF

## Slide 29: It is just like inverter chain!
The only size related par.

## Slide 30: Designing Fast Circuits
Delay is smallest when each stage bears same effort
Thus minimum delay of N stage path is
This is a key result of logical effort
  Find fastest possible delay
  Doesn’t require calculating gate sizes

## Slide 31: Gate Sizes
How wide should the gates be for least delay?
Working backward/forward, apply capacitance transformation to find input capacitance of each gate given load it drives.

## Slide 32: Example: 3-stage path
Select gate sizes x and y for least delay from A to B

## Slide 33: Example: 3-stage path
Logical Effort G =
Electrical Effort F =
Branching Effort B =
Path Effort H =
Best Stage Effort h=
Parasitic Delay P =
Delay D =

## Slide 34: Example: 3-stage path
Logical Effort G = (4/3)*(5/3)*(5/3) = 100/27
Electrical Effort F =45/8
Branching Effort B =3*2=6
Path Effort H =GBF=125
Best Stage Effort h=H1/3=5
Parasitic Delay P =2+3+2=7
Delay D =3*5+7=22=4.4FIO4

## Slide 35: Example: 3-stage path
Work backward for sizes
y =
x =

## Slide 36: Example: 3-stage path
Work backward for sizes
y = 45 * (5/3) / 5 = 15
x = (15*2) * (5/3) / 5 = 10

## Slide 37: Best Number of Stages
How many stages should a path use?
  Minimizing number of stages is not always fastest
Example: drive 64-bit datapath with unit inverter
D =

## Slide 38: Best Number of Stages
How many stages should a path use?
  Minimizing number of stages is not always fastest
Example: drive 64-bit datapath with unit inverter
D = NH1/N + P
= N(64)1/N + N

## Slide 39: Derivation
Consider adding inverters to end of path
  How many give least delay?
Define best stage effort

## Slide 40: Best Stage Effort
has no closed-form solution
Neglecting parasitics (pinv = 0), find h = 2.718 (e)
For pinv = 1, solve numerically for h= 3.59

## Slide 41: Sensitivity Analysis
How sensitive is delay to using exactly the best number of stages?
2.4 < h< 6 gives delay within 15% of optimal
  We can be sloppy!
  I like h= 4

## Slide 42: Example, Revisited
Ben Bitdiddle is the memory designer for the Motoroil 68W86, an embedded automotive processor. Help Ben design the decoder for a register file.
Decoder specifications:
  16 word register file
  Each word is 32 bits wide
  Each bit presents load of 3 unit-sized transistors
  True and complementary address inputs A[3:0]
  Each input may drive 10 unit-sized transistors
Ben needs to decide:
  How many stages to use?
  How large should each gate be?
  How fast can decoder operate?
Notes: R[0]=~A[3]~A[2] ~A[1]~A[0]
R[1]=~A[3]~A[2] ~A[1] A[0]
R[2]=~A[3]~A[2] A[1]~A[0]

## Slide 43: Number of Stages
Decoder effort is mainly electrical and branching
Electrical Effort: F =
Branching Effort: B =
If we neglect logical effort (assume G = 1)
Path Effort: H =
Number of Stages: N =
Try a 3-stage design

## Slide 44: Number of Stages
Decoder effort is mainly electrical and branching
Electrical Effort: F= (32*3) / 10 = 9.6
Branching Effort: B = 8
If we neglect logical effort (assume G = 1)
Path Effort: H = GBF = 76.8
Number of Stages: N = log4H = 3.1
Try a 3-stage design
Chicken and egg problem

## Slide 45: Gate Sizes & Delay
Logical Effort: G =
Path Effort: H =
Stage Effort: h=
Path Delay: D =
Gate sizes: z = y =

## Slide 46: Gate Sizes & Delay
Logical Effort: G = 1 * 6/3 * 1 = 2
Path Effort: H = GBF = 154
Stage Effort: h =H1/4=3.52 h =H1/3=5.36
Path Delay: D =4h+1+4+1+1=7+14.08=21.1
D =3h+1+4+1=6+16.08=22.1
Gate sizes: z = 96*1/5.36 = 18 y = 18*2/5.36 = 6.7

## Slide 47: Number of Stages
Decoder effort is mainly electrical and branching
Electrical Effort: F= (32*3) / 10 = 9.6
Branching Effort: B = 8
Path Effort: H = GBF = 2*8*9.6=153.6
Number of Stages: N = log4H = 3.6
Try a 3/4-stage design
If we neglect logical effort (assume G = 2)

## Slide 48: Gate Sizes & Delay
Logical Effort: G = 1 * 6/3 * 1 = 2
Path Effort: H = GBF = 154
Stage Effort: h =H1/4=3.52 h =H1/3=5.36
Path Delay: D =4h+1+4+1+1=7+14.08=21.1
D =3h+1+4+1=7+14.08=22.1
Gate sizes: s=96*1/3.52=27; z=27*1/3.52=8; y=8*2/3.52=5
z = 96*1/5.36 = 18 y = 18*2/5.36 = 6.7

## Slide 49: Comparison
Compare many alternatives with a spreadsheet
Design | N | G | P | D
NAND4-INV | 2 | 2 | 5 | 29.8
NAND2-NOR2 | 2 | 20/9 | 4 | 30.1
INV-NAND4-INV | 3 | 2 | 6 | 22.1
NAND4-INV-INV-INV | 4 | 2 | 7 | 21.1
NAND2-NOR2-INV-INV | 4 | 20/9 | 6 | 20.5
NAND2-INV-NAND2-INV | 4 | 16/9 | 6 | 19.7
INV-NAND2-INV-NAND2-INV | 5 | 16/9 | 7 | 20.4
NAND2-INV-NAND2-INV-INV-INV | 6 | 16/9 | 8 | 21.6

## Slide 50: Review of Definitions
Term | Stage | Path
number of stages | N | 
logical effort | g | 
electrical effort | f = Cout/Cin | F= Cout-path/Cin-path
branching effort |  | 
effort | h =gf | H=GBF
effort delay | h | 
parasitic delay | p | 
delay | d = p+f | 

## Slide 51: Method of Logical Effort
Compute path effort H=GBF(G=1)
Estimate best number of stages N=log4H
Sketch path with N stages
Re-compute G
Determine best stage effort h=GBF1/N=H1/N
Estimate least delay D=P+h*N
Find gate sizes

## Slide 52: Limits of Logical Effort
Chicken and egg problem
  Need path to compute G
  But don’t know number of stages without G
Simplistic delay model
  Neglects input rise time effects
Interconnect
  Iteration required in designs with wire
Maximum speed only
  Not minimum area/power for constrained delay

## Slide 53: Summary
Numeric logical effort characterizes gates
NANDs are faster than NORs in CMOS
Paths are fastest when effort delays are ~4
Path delay is weakly sensitive to stages, sizes
Using fewer stages doesn’t mean faster paths
Delay of path is about log4H stage

## Slide 54: Example 1
module mux(input s, d0, d1,
output y);
assign y = s ? d1 : d0;
endmodule
1) Sketch a design using AND, OR, and NOT gates.

## Slide 55: Example 1
module mux(input s, d0, d1,
output y);
assign y = s ? d1 : d0;
endmodule
1) Sketch a design using AND, OR, and NOT gates.

## Slide 56: Example 2
2) Sketch a design using NAND, NOR, and NOT gates. Assume ~S is available.

## Slide 57: Example 2
2) Sketch a design using NAND, NOR, and NOT gates. Assume ~S is available.

## Slide 58: Bubble Pushing
Start with network of AND / OR gates
Convert to NAND / NOR + inverters
Push bubbles around to simplify logic
  Remember DeMorgan’s Law
Head bubbles
Tail
bubbles

## Slide 59: Example 3
3) Sketch a design using one compound gate and one NOT gate. Assume ~S is available.

## Slide 60: Example 3
3) Sketch a design using one compound gate and one NOT gate. Assume ~S is available.

## Slide 61: Example 4
The multiplexer has a maximum input capacitance of 16 units on each input. It must drive a load of 160 units. Estimate the delay of the NAND and compound gate designs.

## Slide 62: Example 4
The multiplexer has a maximum input capacitance of 16 units on each input. It must drive a load of 160 units. Estimate the delay of the NAND and compound gate designs.
F = 160 / 16 = 10
B = 1
N = 2
PK

## Slide 63: NAND Solution

## Slide 64: Compound Solution

## Slide 65: Compound Solution

## Slide 66: Example 5
Annotate your designs with transistor sizes that achieve this delay.

## Slide 67: Example 5
Annotate your designs with transistor sizes that achieve this delay.
Notes: Right figure compound gate 36*2/4.5=8/0.5=16
2/a=4/b ,b=2a
A+b=16

## Slide 68: Another application
Example 4.15
The circuit in Figure 4.37 has nonuniform branching, reconvergent fanout, and a wire
load in the middle of the path, all of which stymie back-of-the-envelope application of
Logical Effort. The wire load is given in the same units as the gate capacitances (i.e.,
multiples of the capacitance of a unit inverter). Assume the inputs arrive at time 0.
Write an expression for the arrival time of the output as a function of the gate drives.
Determine the sizes to achieve minimum delay.

## Slide 69: Another application
gi.xi.Cref-inverter
xi means xi times of unified logic
gN+1=1

## Slide 70: Another example of Rabaey.Textbook
F=5,G=1*5/3*5/3*1,B=1
H=GBF=125/9, h=H1/4=1.93
h=gifi=gi *gi+1xi+1/gixi=gi+1xi+1/xi
xi= gi+1xi+1 /h
c=5/1.93=2.59
b=1*2.59/1.93=1.34
a=5/3*1.34/1.93=1.16
h=gifi=gi *gi+1xi+1/gixi=gi+1xi+1/xi
xi+1 = xi h/gi+1 = xi gifi /gi+1
=xi-1 gifi gi-1fi-1 / gi gi+1
= x1 f1 …fi / gi+1
a=1.93/5/3=1.16
b=1.16*1.93/5/3=1.34
c=1.34*1.93/1=2.59
Notes: Textbook its ithlogic size define as gi.si.Cref-inverter
We just call Ci=riCref-inverter-RC=ri/3 Cref-inverter

## Slide 71: Another application
In paths that branch, each fork should contribute equal delay. If one fork were faster than the other, it could be downsized to reduce the capacitance it presents to the stage before the branch.
The stage efforts, f, are equal for each gate in paths with no fixed capacitive loads,but may change after a load.
To minimize delay, upsize gates on nodes with large fixed capacitances to reduce the effort borne by the gate, while only slightly increasing the effort borne by the predecessor.

## Slide 72: Logic effort is related with… …
Transistor’s size?
the special Path?
the special edge?

## Slide 73: Asymmetric Gates
Asymmetric gates favor one input over another
Ex: suppose input A of a NAND gate is most critical
  Use smaller transistor on A (less capacitance)
  Boost size of noncritical input
  So total resistance is same
gA =
gB =
gtotal =
Asymmetric gate approaches g = 1 on critical input
But total logical effort goes up

## Slide 74: Asymmetric Gates
Asymmetric gates favor one input over another
Ex: suppose input A of a NAND gate is most critical
  Use smaller transistor on A (less capacitance)
  Boost size of noncritical input
  So total resistance is same
gA = 10/9
gB = 2
gtotal = gA + gB = 28/9
Asymmetric gate approaches g = 1 on critical input
But total logical effort goes up
the special Path Optimization

## Slide 75: Skewed Gates
Skewed gates favor one edge over another
Ex: suppose rising output of inverter is most critical
  Downsize noncritical nMOS transistor
Calculate logical effort by comparing to unskewed inverter with same effective resistance on that edge.
  gu =
  gd =

## Slide 76: Skewed Gates
Skewed gates favor one edge over another
Ex: suppose rising output of inverter is most critical
  Downsize noncritical nMOS transistor
Calculate logical effort by comparing to unskewed inverter with same effective resistance on that edge.
  gu = 2.5 / 3 = 5/6
  gd = 2.5 / 1.5 = 5/3
the special Edge Optimization

## Slide 77: HI- and LO-Skew
Def: Logical effort of a skewed gate for a particular transition is the ratio of the input capacitance of that gate to the input capacitance of an unskewed inverter delivering the same output current for the same transition.
Skewed gates reduce size of noncritical transistors
  HI-skew gates favor rising output (small nMOS)
  LO-skew gates favor falling output (small pMOS)
Logical effort is smaller for favored direction
But larger for the other direction

## Slide 78: Catalog of Skewed Gates

## Slide 79: Catalog of Skewed Gates

## Slide 80: Catalog of Skewed Gates

## Slide 81: Combine asymmetric and skewed gates
  Downsize noncritical transistor on unimportant input
  Reduces parasitic delay for critical input
4
  critical transistor on important input
  Hiskew for the special path

## Slide 82: Best P/N Ratio
We have selected P/N ratio for unit rise and fall resistance (m = 2-3 for an inverter).
Alternative: choose ratio for least average delay
Ex: inverter
  Delay driving identical inverter
  tpdf =
  tpdr =
  tpd =
  Differentiate tpd w.r.t. P
  Least delay for P =

## Slide 83: Best P/N Ratio
We have selected P/N ratio for unit rise and fall resistance (m = 2-3 for an inverter).
Alternative: choose ratio for least average delay
Ex: inverter
  Delay driving identical inverter
  tpdf = (P+1)
  tpdr = (P+1)(m/P)
  tpd = (P+1)(1+m/P)/2 = (P + 1 + m + m/P)/2
  Differentiate tpd w.r.t. P
  Least delay for P =

## Slide 84: P/N Ratios
In general, best P/N ratio is sqrt of equal delay ratio.
  Only improves average delay slightly for inverters
  But significantly decreases area and power

## Slide 85: P/N Ratios
In general, best P/N ratio is sqrt of that giving equal delay.
  Only improves average delay slightly for inverters
  But significantly decreases area and power

## Slide 86: Observations
For speed:
  NAND vs. NOR
  Many simple stages vs. fewer high fan-in stages
  Latest-arriving input
For area and power:
  Many simple stages vs. fewer high fan-in stages